SECTION 09843 – HANGING ACOUSTICAL COTTON BAFFLES

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

SUMMARY

This Section includes bonded acoustical cotton used as hanging baffle.

SUBMITTALS

Product Data: Submit manufacturer's product data and installation instructions.

[LEED Submittals: Product data showing recycled content.]

Samples: Submit 2 samples of 6" x 6", showing full range of exposed texture to be expected in completed work.

Test Reports: Upon request submit certified test reports from recognized test laboratories.

Certificates: Submit manufacturer's certificate that products meet or exceed specified requirements.

QUALITY ASSURANCE

Installer Qualifications: Utilize an installer having demonstrated experience on projects of similar size and complexity.

DELIVERY, STORAGE & HANDLING

Delivery: Deliver material in the manufacturer’s original, unopened, undamaged containers with identification labels intact.

Provide labels indicating brand name, source of procurement, style, size and thickness.

Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

MAINTENANCE

Extra Materials: Provide [Specify percentage] for use by owner in building maintenance and repair.

Provide new unopened cartons of extra materials, packaged with protective covering for storage and identified with appropriate labels.

WARRANTY

Warranty Period:  One year.

PRODUCTS

MANUFACTURERS

Hanging Acoustical Cotton Baffles:

Echo Eliminator by Acoustical Surfaces Inc. (Basis of Design)

123 Columbia Court North Suite 210.

Chaska, MN  55318

(800) 448 - 0121.

www.AcousticalSurfaces.com

Or equal.

HANGING ACOUSTICAL COTTON BAFFLES

Material: Bonded acoustical cotton. 100% recyclable, fiberglass free, high performance, durable, and lightweight.

Pattern: Soft textured surface.

Applications: Gymnasiums, auditoriums, classrooms, music rooms, arenas, stadiums, churches, offices, computer rooms, restaurants/cafeterias, residential, concert halls & theaters, pro audio, gun ranges, manufacturing plants, machine enclosures, and water treatment plants.

Thickness: 1 inch and 2 inches.

Sizes: 2’ x 4’, custom sizes & die cut parts available.

Color: [White] [Marble Light Blue] [Light Grey] [Charcoal] [Pure Blue] [Navy Blue] [Burgundy] [As selected by Architect].

Grommet Color: [Gold] [Silver] [As selected by Architect].

Flammability:

ASTM E84, Class A. Flame Spread: 5.

Smoke Developed: 35.

Acoustical Absorption Performance:

1 inch thick 2’ x 4’ baffle: Average 10.30 Sabins.

2 inch thick 2’ x 4’ baffle: Average 13.85 Sabins.

EXECUTION

EXAMINATION

Site Verification of Conditions:

Examine surfaces scheduled to receive furred out or directly attached acoustical units for unevenness, irregularities and dampness that would affect quality and execution of work.

Do not proceed with installation of acoustical panels until unacceptable conditions are corrected.

Environmental Requirements:

Do not install acoustical panels until building is closed in and HVAC system is operational.

INSTALLATION

General: Do not begin installation until materials sufficient to complete an entire room are received and are ready for installation.

Field cut acoustical panels as required, in accordance with manufacturers recommended procedures and equipment.

Install acoustical wall panels in accordance with quantity and lay-outs as shown on the architectural drawings.

Acoustical wall panels shall be adhesively or mechanically mounted in accordance with manufacturer’s recommendations and/or as detailed on the drawings.

Manufacturer’s Instructions:

Comply with the instructions and recommendations of the acoustical panel manufacturer.

Install materials in accordance with governing regulations, fire resistance rating requirements and industry standards applicable to work.

CLEANING

Clean exposed surfaces of acoustical panel to comply with manufacturer's instructions for cleaning.

Remove and replace tiles, which cannot be successfully cleaned and repaired to permanently eliminate evidence of damage.

PROTECTION

Protect installed work from damage due to subsequent construction activity, including temperature and humidity limitations and dust control, so that the work will be without damage and deterioration at the time of acceptance by the Owner.

END OF SECTION 09843